## Slide 1: Lab2
איליה זלדנר

## Slide 2: Interrupt Vector Table
In Interrupt Vector Table in 00000h-003FFh (1KB)
For the execution of INT 00-FF
Each INT uses a 4-byte vector (CS:IP):
  2 bytes for IP
  2 bytes for CS
Actual code (Service Routine) is in CS:IP
IRET at the end of INT Service Routine

## Slide 3: Interrupt Vectoring Process

## Slide 4
Step 1:
  The operand of INT is multiplied by 4 to locate the matching interrupt vector table entry
Step 2:
  CPU pushes flags and a 32-bit return address on stack, disables hardware interrupts, and calls using the address stored at location (10h * 4) in the interrupt vector table (F000:F065)
Step 3:
  Interrupt handler executes until IRET is reached
Step 4:
  Pop the stack and return to application program

## Slide 5: STI (Set Interrupt Flag)
Opcode : FB
Description : Set interrupt flag; external, maskable interrupts enabled at the end of the next instruction.
If protected-mode virtual interrupts are not enabled, STI sets the interrupt flag (IF) in the EFLAGS register. After the IF flag is set, the processor begins responding to external, maskable interrupts after the next instruction is executed. The delayed effect of this instruction is provided to allow interrupts to be enabled just before returning from a procedure (or subroutine). For instance, if an STI instruction is followed by an RET instruction, the RET instruction is allowed to execute before external interrupts are recognized.

## Slide 6: CLI(Clear Interrupt Flag)
Opcode : FA
Description : Clear interrupt flag; interrupts disabled when interrupt flag cleared.
If protected-mode virtual interrupts are not enabled, CLI clears the IF flag in the EFLAGS register. No other flags are affected. Clearing the IF flag causes the processor to ignore maskable external interrupts. The IF flag and the CLI and STI instruction have no affect on the generation of exceptions and NMI interrupts.

## Slide 7: How the keyboard works
Keyboard controller chip sends an 8-bit scan code to the keyboard serial input port
Interrupt triggered, INT 9h routine executes
Scan code and ASCII code inserted into keyboard typeahead buffer

## Slide 8: Keyboard Flags
16-bits, located at 0040:0017h – 0018h

## Slide 9: IN(Input from Port)
Description : Copies the value from the I/O port specified with the second operand (source operand) to the destination operand (first operand). The source operand can be a byte-immediate or the DX register; the destination operand can be register AL, AX, or EAX, depending on the size of the port being accessed (8, 16, or 32 bits, respectively). Using the DX register as a source operand allows I/O port addresses from 0 to 65,535 to be accessed; using a byte immediate allows I/O port addresses 0 to 255 to be accessed.
Opcode | Mnemonic | Description
E4 ib | IN AL,imm8 | Input byte from imm8 I/O port address into AL.
E5 ib | IN AX,imm8 | Input byte from imm8 I/O port address into AX.
E5 ib | IN EAX,imm8 | Input byte from imm8 I/O port address into EAX.
EC | IN AL,DX | Input byte from I/O port in DX into AL.
ED | IN AX,DX | Input word from I/O port in DX into AX.
ED | IN EAX,DX | Input doubleword from I/O port in DX into EAX.

## Slide 10: OUT(Output to Port)
Description : Copies the value from the second operand (source operand) to the I/O port specified with the destination operand (first operand). The source operand can be register AL, AX, or EAX, depending on the size of the port being accessed (8, 16, or 32 bits, respectively); the destination operand can be a byte-immediate or the DX register. Using a byte immediate allows I/O port addresses 0 to 255 to be accessed; using the DX register as a source operand allows I/O ports from 0 to 65,535 to be accessed.
Opcode | Mnemonic | Description
E6 ib | OUT imm8, AL | Output byte in AL to I/O port address imm8.
E7 ib | OUT imm8, AX | Output word in AX to I/O port address imm8.
E7 ib | OUT imm8, EAX | Output doubleword in EAX to I/O port address imm8.
EE | OUT DX, AL | Output byte in AL to I/O port address in DX.
EF | OUT DX, AX | Output word in AX to I/O port address in DX.
EF | OUT DX, EAX | Output doubleword in EAX to I/O port address in DX.

## Slide 11: Port
External devices are almost always connected not directly to the system bus but to an INTERFACE.
Registers in the interface allow for a wide range of possibilities for the designer to determine how it is to interface to the bus.
To avoid confusion with the main registers in the 8086, peripheral interface chip registers are usually referred to as PORTS.

## Slide 12: Interface Ports
Typically consists of three registers
  Control Port - the setting of which will determine if the interface is to send or receive.
  Data Port – for the data element to be transmitted or to hold a data element received.
  Status Port – used to obtain information such as “printer out of paper, don’t send any more data” or, for a serial transmission, “all the bits of the data element haven’t yet been received”
  Simple interfaces may have status and control combined into one port; sophisticated ports may have multiple control and status ports.

## Slide 13: Scan Code
For Each Key Scan Code comes Twice once the Key press and once for key release
Both Scan code are differ in one bit
The lower seven bit contain the key number
While the Most Significant bit is clear in the Press code and Set in the Release Code
If we write Capital A so we First Press Shift Key the Scan Code is Sent then We Pressed A Scan Code is Sent then the Release code of A & release code of Shift Key and Interrupt Handler Understand That Sequence Should Result in ASCII Code of A
Interrupt handler REMEMBER the Sequence .

## Slide 14: Keyboard Port
The Keyboard Port is 60 the Keyboard Generate IRQ 1 when Ever Key is Pressed so if we Hooked INT 9 inside the it read Port 60so we can tell Which Key is Pressed
PC keyboard: interrupt driven – Cannot run in polled mode: no status port
2 interrelated 8255 PPI (Parallel Peripheral Interface) ports:
  Data Port (Port PA) : I/O address 60H
  Control Port (Port PB) : I/O address 61H
Keyboard will not send next scan code until previous one “acknowledged”

## Slide 15: Keyboard and its controller
Keyboard Controller
CPU
PIC
bus
KEYBOARD
PS/2 MOUSE
output port
TIMER
output buffer
status reg
control reg
0x64
0x64
0x60
0x60
input buffer
input port
RAM
PIC
IRQ0
IRQ1
IRQ2